Classnote – 2		Air Pollutants

# Particulate Matter

National Ambient Air Quality Standard for Particulate Matter (National Ambient Air Quality Standards for Particulate Matter and Ozone; Final Rules July 18, 1997, 40 CFR Part 50, Section II-H):

- Twenty-four hour average PM2.5 is met when the three-year average of annual 98th percentiles of 24-hr PM2.5 concentrations at each population-oriented monitor within an area is less than or equal to 65 (g/m3, with fractional parts of 0.5 or greater rounding up;

- The annual PM2.5 standard is met when the three-year average of the annual arithmetic mean PM2.5 concentrations, from single or multiple community-oriented monitors is less than or equal to 15 (g/m3, with fractional parts of 0.05 or greater rounding up;

- The 24-hour average PM10 is met when the three-year average of annual 99th percentiles of 24-hr PM10 concentrations at each monitor within an area is less than or equal to 150 (g/m3;

- The annual PM10 standard is met when the three-year average of the annual arithmetic mean PM10 concentrations at each monitor within an area is less than or equal to 50 (g/m3, with fractional parts of 0.5 or greater rounding up.

The first two standards for PM2.5 are new.  The third standard for 24-hour average PM10 is revised to be based on the three-year average of annual 99th percentiles of 24-hr PM10 concentrations at each monitor within an area from “with no more than one expected exceedance per year”.

Along with a National Ambient Air Quality Standard, the measurement instruments, methods, data collection, quality assurance protocols, laboratory methods, laboratory QA/QC, data reporting, time line for compliance.  Many times, the sampling results are not only used for compliance purposes but also for identifying sources, assessing health risks, evaluating effectiveness of control devices, and determining areas of impacts.  Thus, it is important to understand what we actually collect from the samplers.

Ideal PM size distribution with three modes in ambient air

- Nucleation mode: varies from 0.005 to 0.1 (m and peaks at ~ 0.08 (m, accounting for the preponderance of particles by number.  Nucleation particle lifetimes are usually less than 1 hour because they rapidly coagulate with larger particles or serve as nuclei for cloud or fog droplets.

- Accumulation mode: extends from 0.1 to 2.5 (m, which accounts for most of the aerosol (particle) surface areas.   The majority of sulfuric acid, ammonium, bisulfate, ammonium sulfate, ammonium nitrate, organic carbon, and elemental carbon is found in this range.

- Coarse mode (or sedimentation mode): It varies between 2.5 to 25 (m and peaks at around 10(m.  The peak of the coarse mode may shift between 6 and 25 (m depending on the common emission sources in the region.

Major chemical components in PM

- Geologic Elements: Al, Ca, Si, K, P, Na, and other trace elements

- Sulfate: Ammonium sulfate, ammonium bisulfate, sulfuric acid, sodium sulfate

- Nitrate: Ammonium nitrate, sodium nitrate

- Ammonium: Ammonium sulfate, ammonium bisulfate, ammonium nitrate

- Sodium Chloride

- Organic Carbon: compounds containing more than 20 carbon atoms (<C20)

- Element Carbon (soot)

- Liquid Water

### Sampling Technologies

PM exists in the air with various shapes and densities.  No sampling instrument (or at least not developed) can provide stepwise sharp cut of passing 100 % of PM small than a specific size and excluding 100 % of PM large than that specified size.  As a result, the PM samples we collected in the air always include various sizes of PM.  The methods used in PM sampling include inlet size selection, filtration, impaction, virtual impaction, and other technologies based on particle aerodynamics that are applicable in air pollution control.  In any cases, size selective inlets are commonly used in every sampling instrument.

As stated before, sharp size cut-off cannot be achieved.  Therefore, the goal is to develop an inlet that can have as sharp size cut-off as possible.

Size Cut-off: an instrument’s size cut-off is defined by the 50 % cut-point (d50).   d50 represents the aerodynamic diameter at which 50 % of the sampled particles penetrate an inlet.  The effectiveness of the sharp cut-off is defined by the slope of the sample effectiveness (or the ratio of d16/d84).  A slope of 1 indicates that 100 % of the particles with aerodynamic diameter less than the cut-off pass through the inlet to the filter, and 0 % of those larger than the cut-point are collected.  Typical values of the slope vary between 1.3 and 2.  Figure 4.1 of EPA 1997 shows typical characteristics of sampling effectiveness curve for inlets.  Figure 4.2 shows a conceptual graph of PM size distribution collected on filters.  It appears that coarse PM collected on the filters are likely to be attenuated from what actually exist in ambient air.

References

J.C. Chow.  1995.  Measurement methods to determine compliance with ambient air quality standards for suspended particles.  JA&WMA. 45:320-382.

U.S. EPA. 1997.  Draft guideline on speciated particulate monitoring.

U.S. EPA. 1997.  40 CFR Part 50.  National Ambient Air Quality Standards for Particulate Matter and Ozone; Final Rules July 18, 1997.

Nitrogen Containing Compounds

N2:	Major gas in the atmosphere (79 %), stable

Nitrogen is abundant in the atmosphere and is an essential nutrient to all living organisms.  Nitrogen is “fixed” by either microorganisms on earth or ionizing phenomenon in the atmosphere.  Microorganisms in the soil convert nitrogen to ammonia, ammonium ion (NH4+), organic nitrogen compounds.  Atmospheric ionization of nitrogen, through cosmic radiation or lightning, forms various nitrogen oxides.

N2O:	Nitrous Oxide

- Colorless gas released by natural causes

- Products of bacterial action in the soil and in water

- Also known as the laughing gas

- Energy absorption property is 300 times that of CO2

- Inert in the troposphere and reacts with atomic oxygen (O) to form NO in the stratosphere

- Lifetime = 120 + 30 yrs

# NOx:	Nitrogen Oxides (NOx = NO + NO2)

# NOy:	Nitrogen Oxides (NOy = NOx + products of atmospheric oxidation of NOx)

# NOz:	Products of atmospheric oxidation of NOx only (NOz = NOy - NOx)

# Products of Atmospheric Oxidation

# HNO3:		Nitric Acid

- Major oxidation product of NOx

- Water Soluble

- In the presence of NH3, it can form HN4ONO3 aerosol

- Night concentrations are at about 300 pptv

NO3:	Nitrate Radical

N2O5:	Di-Nitrate Pentoxide

HNO4:		Peroxynitric Acid

RC(O)OONO2:	Peroxyacetyl Nitrate (PAN)

# RONO2:		Alkyl Nitrates

# ROONO2:		Peroxyalkyl Nitrates

# NH3:		Ammonia, third most abundant gas of nitrogen

- Readily absorbed by surface

- 10 days residence time in the atmosphere

- Removed by wet and dry deposition

- Background concentration ranges from 0.1 to 10 ppbv

Atmospheric cycle of nitrogen compounds

Sulfur-Containing Compounds

- Common atmospheric sulfur compounds: H2S, CH3SCH3, CS2, OCS, and SO2

- Chemical reactivity of atmospheric sulfur compounds is inversely related to their sulfur oxidation state.  For example, H2S (oxidation state of –2) is much more reactive than SO2 (oxidation state of +4)

- Hydrogen sulfide, H2S, is a colorless gas with a strong odor of rotten eggs.  It’s also commonly know as sewer gas

- Dimethyl sulfide, CH3SCH3, is the dominant sulfur compound emitted from the oceans.  Imbalance of CH3SCH3 results in continuous emissions of dimethyl sulfide from the oceans.

- Carbonyl sulfide, OCS, naturally exists in the atmosphere and is the only sulfur compound survives to enter into the stratosphere.

- Sulfur dioxide, SO2, is the predominant antorpogenic sulfur-containing compounds and is one of the criteria pollutants regulated by the U.S. EPA.

Carbon-Containing Compounds

•Lewis Structures: They help us visualize how atoms connect with each other by either sharing electrons (covalent bond) or losing / gaining electrons (ionic bond) as to achieve an octet of electros therefore resembling the noble gases.

H

• •

H • • C • • H

• •

H

Lewis Representation of methane

•Isomers: Compounds having the same molecular formula, but different structural formula (different connectivity between atoms).

Example

CH3-CH2-CH2-CH3                                CH3

butane			           |

CH3-CH-CH3

isobutane

•Alkanes and Alkenes (open-chain)

Hydrocarbons in which each carbon atom forms four single bonds to other atoms are called saturated hydrocarbons, paraffins, or alkanes. Hydrocarbons that have at least two carbon atoms joined by a double bond are called undersaturated or alkenes.

Methane:

Ethane:

Propane:

Butane:

Pentane:

Hexane:

Heptane:

Aromatic hydrocarbons (close-chain) are benzene compounds and compounds that resemble benzene in chemical behavior

•Example of important alkanes and alkenes on the environment as well as aromatic hydrocarbons.

CCl3-CH3			           CH2Cl-CH2Cl

1,1,1-Trichloroethane (TCA)		1,2-Dichloroethane (1,2-DCA)

CCl2F-CF2Cl

1,1,2-Trichloro-1,2,2-trifluroethane

CH2=CH2			           CCl2=CHCl

Ethyne (ethylene)			Trichloroethylene (TCE)

•Nomenclature of open-chain compounds:

- Find the longest continuous chain of carbon atoms. Assign a parent name based on total number of carbons.

- Find whatever groups are not part of the longest continuous chain. Name these prefixes

- Assign numbers to groups by counting from one end of the chain. A chain has two ends, and the end we start from is the one that gives the lowest possible numbers to the groups.

- If there are two or more identical groups, we use these prefixes:

Number of identical groups	prefix

2			di

3			tri-

4			tetra-

5			penta-

6			hexa-

5.

If there are two or more different groups, we put all of them into the prefix in alphabetical order.

- The four halogens are named by prefixes:

F fluoro-		Br bromo-

Cl chloro-		I    Iodo-

Answer: 	Heptane ( 2,5 dichloro ( 2-methyl ( 4-ethyl

( 2,5-dichloro-4-ethyl-2-methyl-heptane

- Methane

- Volatile Organic Compounds (VOCs)

Aromatic Compounds

Nomeclature of benzene derivatives (aromatic):

-prefix the name of the substituent group to the word –benzene

Ex.

(a)                    (b)                  (c)                (d)                  (e)                  (f)

a- Chlorobenzene

b-Bromobenzene

c- Nitrobenzene

d- methylbenzene (Toluene)

e- aminobenzene (Aniline)

f- hydroxybenzene (Phenol)

•Nomenclature if several are attached to the benzene ring

-We must not only tell what they are, but also indicate their relative positions.

Ex.

o- ortho position

m- meta position

p- para position

a	       	        b	   		c

Name

a) 2- Chloronitrobenzene or o-chloronitrobenzene

b) 4-Bromomethylbenzene or 4-Bromotoluene or p-Bromotoluene

c) 2,4,6-triiodohydroxybenzene or 2,4,6-triiodophenol

- Methane (CH4)

- Volatile Organic Compounds (VOCs)

- Biogenic Hydrocarbons

- Carbon Monoxide

Carbon monoxide is a colorless and odorless gas.  It is very stable and has a lifetime of 2 to 4 months in the atmosphere.  There are many studies that show that high concentrations of CO can cause physiological and pathological changes and also ultimately death.  CO is a poisonous inhalant that deprives the body tissues of necessary oxygen.  At high concentration (>750 ppmv), it is known to cause death.  Dissolved CO combines with hemoglobin to form caboxyhemoglobin (COHb) in the blood and thus reduces the oxygen carrying capacity of blood.

- Carbon Dioxide

Halogen-Containing Compounds

- Chlorofluorocarbons (CFCs)

- Hydrochlorofluorocarbons (HCFCs)

- Hydrofluorocarbons (HFCs)

- Perhalocarbons: halocarbons in which every available carbon bond contains a halogen atom (compounds saturated with halogen atoms)

- Halons (bromine-containing halocarbons, especially used as fire extinguishing agents

COHb in blood due to exposures to CO

### Health effects associated with CO exposures

Health effects associated with the level of COHb in blood

Ozone

Health and environmental effects associated with ozone exposures

Methemoglobinemia

Nitrate, a relatively non-toxic substance, occurs naturally as part of the nitrogen cycle. However, bacteria can convert nitrate to nitrite in the environment, in foods and in the human body.

Until infants reach about six months of age, their digestive system secretes lower amounts of gastric acid and the pH level in their digestive system is higher than most adults. Adults with a diminished capability to secrete gastric acid also can experience a rise in pH in their digestive system. In both situations, bacteria can proliferate, increasing the transformation of nitrate to nitrite.

Once in the blood, nitrite oxidizes iron in the hemoglobin of red blood cells to form methemoglobin, which lacks hemoglobin's oxygen-carrying ability. The nitrite can come from nitrate in drinking water or from food, some drugs or other sources.

Although methemoglobin is continually produced in humans, an enzyme in the human body reduces methemoglobin to hemoglobin. In most individuals, methemoglobin is rapidly converted back to hemoglobin. Typically, less than 1 percent of the total circulating hemoglobin in a healthy adult is present in the form of methemoglobin. Infants, however, have a low concentration (about 60 percent of the adult concentration) of the reducing enzyme, as do some older individuals with an enzyme deficiency. In these people, methemoglobin is not converted to hemoglobin as readily.

When methemoglobin levels are elevated, the condition known as methemoglobinemia, often referred to as "blue baby syndrome", can result as the blood lacks the ability to carry sufficient oxygen to individual body cells.

- Methemoglobinemia Signs and Symptoms

Infants suffering from methemoglobinemia may seem healthy but show intermittent signs of blueness around the mouth, hands and feet. They may have episodes of breathing trouble, some diarrhea and vomiting. In some cases, an infant with methemoglobinemia has a peculiar lavender color but shows little distress. Blood samples appear chocolate brown and don't turn pink when exposed to air. When the methemoglobin level is high, infants express a marked lethargy, excessive salivation and loss of consciousness. Convulsions and death can occur at extreme methemoglobin levels.

- Methemoglobinemia Case Histories

Cases of infant methemoglobinemia have been reported in the United States. The majority of reported cases were in infants under the age of four months and who were fed milk formulas prepared with contaminated well water. A Nebraska survey of physicians reported in the Nebraska Medical Journal in 1981 indicated at least eight cases of infant methemoglobinemia were treated in Nebraska between 1973 and 1978. More recently, two infants with methemoglobinemia were identified by the South Dakota Department of Health. The private well water was found to have a nitrate-nitrogen concentration of 150 mg/l in one instance and 54 mg/l in the other. In Colorado, a case of methemoglobinemia involved an infant ingesting water containing 13.3 mg/l nitrate-nitrogen. No cases have been identified with water at or below the MCL of 10 mg/l nitrate-nitrogen.

Source: http://www.ianr.unl.edu/pubs/water/g1369.htm#meth

Atmospheric Residence Times

-                             +                               -                                  =

Where	Q =  Total mass of the substance in the control volume

Fin = Rate of the species flowing in

Fout = Rate of the species flowing out

P = Rate of emission of the species

R = Rate of removal of the species

For steady-state condition,

or

The average residence time, (,

Assuming there is no substances coming in or getting out of the atmosphere, Fin = Fout = 0.  Thus,

A general form of the expression for a pollutant is:

Where pollutants flowing in and out are zeros if we treat the earth atmospheric as one closed system and Pi and Ri consist of the following contributions:

Pin:  Natural emissions

Pia:  Anthropogenic emissions

Pic:  Emissions due to chemical reaction

Rid:  Removal by dry deposition

Riw:  Removal by wet deposition (precipitation scavenging)

Ric:  Removal due to chemical reaction

Rit:  Transport to the stratosphere

If one assumes that removal follows the first-order decay, R=kQ, we have

Thus, the residence time for a species at steady-state becomes

# Text boxes

Rate of the species flowing in

Rate of the species flowing out

Rate of emission of the species

Rate of removal of the species

Rate of accumu. of the species in the control volume